## Slide 1: Park n' Go Final Proposal
Rajdeep Singh
Alexander Huttunen
Jisoo Jung
Yaning (Nina) Yang

## Slide 2: Selected Sensors
Magnetometer

## Slide 3: Problem
Underutilized parking space in underground garage
  Affects surrounding residence price
Knowing the parking availability in the parking garage
  Detecting whether or not an individual parking spot is occupied
  Must be
    Cost Effective
    Low Power
    Reliable

## Slide 4: Sensor: Magnetometer
Measures disturbances in the magnetic field
Almost all vehicles are made of or contain metal of some sort
Place one at the end of each parking spot to detect the car passing into the spot or out.
NXP (a semiconductor manufacturer) has tested this use case and found that it works. (see right)
Car Driving Over Magnetometer
http://blog.nxp.com/connected-car/howto-detect-vehicle-presence-or-movements-with-magnetometers/

## Slide 5: Limitations/ Assumption: Magnetometer
Assumptions:
  Vehicle must be metal of some kind
  Vehicle height is relatively low (less than 3 feet)
  Vehicle drives over the sensor
Limitations:
  If the car enters the parking spot from an unexpected direction

## Slide 6: Strength
Cost efficient, estimated to cost less than $10 per parking spot
Environment
  Weather
  lighting
Location
  Parking garage
  Street parking
Orientation
  Straight/ Parallel/ Diagonal

## Slide 7: Risk: Magnetometer
Magnetometer's data shows some fluctuations, which needed to be filtered somehow. The plot below shows an example of this.
Needs continuous power to be able to be ready for a vehicle to pass over
Possibility of only having one shot at detecting when a car drives over the sensor
Chart: Magnetometer X Axis

## Slide 8: Sensor Comparison (using an Arduino Yun and a piece of metal equipment)
Chart: Magnetometer X Axis
Chart: Magnetometer Z Axis

## Slide 9: Real Car Data
Much smaller amplitude
X-axis is lower when car is over sensor
Mirrored signals

## Slide 10: Design System
Magnetometer
I2C
Si4010 Microcontroller
GNURadio
Graphical User Interface
Frequency Shift Keying (FSK) Signals
Web Server and Database

## Slide 11: Milestones
Trying the magnetometer out with an actual vehicle to assess feasibility
Achieving I2C communication between the Si4010 and magnetometer and processing the signal to detect a car
Radioing a signal back to the Pi from the Si4010 and processing it to the Pi