## Slide 1: Park n' Go
Nina Yang
Alex Huttunen
Jisoo Jung
Rajdeep Singh

## Slide 2: Overall Idea
Sense cars in individual parking spots
Sensors placed under vehicles
Sensors are wireless
Base station placed on each level
Information available via the internet

## Slide 3: System Architecture
Magnetometer
Si4010 Microcontroller
GNURadio
Graphical User Interface
Frequency Shift Keying (FSK) Signals
Web Server and Database

## Slide 4: Sensor: Magnetometer
Measures disturbances in the magnetic field
Almost all vehicles are made of or contain metal of some sort
Place one at the end of each parking spot to detect the car passing into the spot or out.
NXP (a semiconductor manufacturer) has tested this use case and found that it works [1].
[1] http://blog.nxp.com/connected-car/howto-detect-vehicle-presence-or-movements-with-magnetometers/

## Slide 5: Base Station Communication
FSK Radio Signal
  433 MHz (but configurable)
Received by RTL2832U
  TV Tuner - $10.80
  Used as Software Defined Radio
Processing done on Raspberry Pi
  Radio decoding done in Python
  Takes radio packets and displays them using a webserver.
  Connected to Internet via Ethernet or WiFi

## Slide 6: Packet Receive – Console Output
Each sensor has a unique ID
Battery voltage
  Know battery life
Temperature
Packet number
  Signal strength
Car detection result
Sent at regular intervals

## Slide 7: User Interface

## Slide 8: Vehicle Detection
Initial detection approach – detect sudden changes in the signal.
This approach worked, however, there were some limitations.
Limitations were:
  It required the system to be powered 24/7.
  Algorithm itself was complicated.
We needed an algorithm that would be power efficient.

## Slide 9: Vehicle Detection
Get Calibration Data
  Calculate signal average (in x, y, z direction)
  during initial setup
Calculate Threshold
  Multiple trials to calculate threshold
Calculate Signal Difference
  If (current signal – signal average) > threshold
  vehicle is present
This algorithm does not requires system to be powered 24/7 and is less complicated.
Mag
Graph of magnetometer reading
Threshold

## Slide 10: Detection Results
Hyundai

## Slide 11: Development Environment

## Slide 12: PCB Design

## Slide 13: PCB (without/with soldered components)

## Slide 14: Final Look (prototype)

## Slide 15
Overall Setup

## Slide 16: Capitol Hill Testing
Sensor accurately detected car state.
Radio communication was weak.
Notes: a

## Slide 17: Limitations and Assumptions: Magnetometer
Assumptions:
  Vehicle must be metal of some kind
  Vehicle height is relatively low (less than 3 feet)
  Vehicle drives over the sensor
Limitations:
  If the car enters the parking spot from an unexpected direction
  Signal strength weakens as the sensor is far away from the base station
    PCB antenna only provided a range of 17 meters (untuned)
  Vehicle on top of the sensor interferes signal strength

## Slide 18: Advantages
Approximate cost per system is $10 per parking spot.
Long battery life: ~1.4 years waking up every 5 minutes on two AAA batteries.
Standby mode consumes 1.33 uA
We can see all the parking spots available in real-time
System can detect cars as well as motorcycles
Easy installation/replacement – system can be insert underneath a traffic reflector.
Notes: .017A .5 seconds
.031A .5 seconds
1 second 3.0v = .024A = 24mA for 1 second when transmitting
1.33uA si4010 and Magnetometer standby
5min wakeup 24mA every 5min for 1 seconds
5 min = 300 seconds
(299/300) 1.33uA + (1/300) 24mA = Avg Amps = 81.3256uA for 5min wakeup
AAA capacity = 1000 mAh
1000e-3 / 81.3256e-6 = 12296.25hours
1.40368 years.

## Slide 19: Questions?